M5b Z80 BANKED MONITOR
                             (ZBMx)
                          Version 1.22 

                           USER GUIDE

                        November 23,1990

                             Rev. A
                         January 5,1991



                         GRH Enterprises
                        1129 Stonylake Ct
                          Sunnyvale, CA

.PAŠ.HE                        TABLE OF CONTENTS

1.   Overview

2.   Hardware Description

3.   Software Description

4.   Rom Modules

5.   Monitor Function Call Facility

6.   Debugger Commands

.PAŠ.HE                          1.  OVERVIEW

     Thå M5â Systeí Monitoò ió á systeí oæ softwarå anä  hardwarå �
tï supporô thå computeò systeí hardwarå resources® Iô ió designeä �
tï  bå  softwarå  interfacå  anä  hardwarå  flexiblå  foò  futurå �
expansion¬ experimentation¬ anä maintenancå wheî hardwarå wilì bå �
harä tï finä foò thió olä system.

     The Monitor is designed with the following features:

     * CP/M 3.x compatability.
     * Banked memory support.
     * Multiple processor support (Super S100).

     Thió  versioî  ió  aî  interií versioî untiì  releaså  ²  ió �
finished.
.PAŠ.HE                    2.  HARDWARE DESCRIPTION

     The M5b hardware to support the System Monitor includes:

     ª  Z8°  CPÕ  carä  witè:
          - Residenô  2ë bytå ROÍ allwayó aô F800..FFFFè.�
          - Reseô bootstrað circuitry.
          - Banked (24 bit) addressing.

     * Monitor II card
          - Eight 2k x 8 ROMs all located at F800h.
          - Common RAM from E000h thru F7FFh


     The memory map for the system is:
Start   Last        Label     Use
000000..DFFFFF                Motorola MC68010 CPU
E00000..EFFFFF                Intel 80286 CPU
F00000..F7FFFF                Reserved
F80000..F8FFFF      Z80BNK0   Z80 Bank 0
F90000..F9FFFF      Z80BNK1   Z80 Bank 1
FA0000..FAFFFF      Z80BNK2   Z80 Bank 2
FB0000..FDFFFF                Reserved
FE0000..FE7FFF      ROMBNK    32k ROM card
FE8000..FE83FF                Jade 8" Floppy Controller
FE8400..FE87FF                Jade 5" Floppy Controller
FE8800..FE8BFF                Jade 3" Floppy Controller
FE8C00..FEFFFF                Reserved
FF0000..FFFFFF                Motorola MC68010 I/O space

.paŠ     Thå  followinç  describeó thå Pagå ° addresseó  reserveä  iî �
each Z80 bank:

xxxx      Use
0..2      Cold reset (RST 0)
3         CP/M IOBYTE (Not used)
4         CP/M Default Disk
5..7      CP/M System Call
8..A      Debugger breakpoint (RST 8)
B
C
D
E
F
10..12    (RST 16)
13
14
15
16
17
18..1A    (RST 24)
1B        Reserved
1C..1D    Stack pointer for this bank (saved when bank swapped)
1E        Reserved
1F        Reserved
20..22    (RST 32) Monitor System Call facility
23
24..26    (8085 TRAP)
27
28..2A    (RST 40)
2B
2C..2E    (8085 RST 5.5)
2F
30..32    (RST 48)
33
34..36    (8085 RST 6.5)
37
38..3A    CP/M DDT & SID Breakpoint (RST 56)
3B
3C..3E    (8085 RST 7.5)
3F
40..4F    BIOS reserved
50..5B
5C..7F    CP/M-80 File Control Block
80..FF    CP/M-80 Default sector buffer

.PAŠ.HE                    3.  SOFTWARE DESCRIPTION

     Thå  Monitoò  softwarå  ió  devideä  uð  intï  logicaì  tasë �
modules® Thió allowó changeó tï causå thå minimuí impacô tï otheò �
moduleó withiî thå system® Thå interfacå tï theså moduleó wilì bå �
a standard for as long as possible.

     These modules are made up of the following files:

ZBMR.*
     Thió  modulå containó thå ROÍ residenô codå in ROM 0.

     * The Cold Reset initialization vector.
     * The Monitor System Call facility.
     * The default interrupt tables and handlers.
     * The Banked Memory support procedures.
     * Debugger Breakpoint handler.
     * Processor selection (SS100).


ZBMD.*
     Thió  modulå containó thå Z8° debuggeò code®  Iô resideó  iî �
ROÍ  £  3 (F800..FFFFh© iî  thå  ROÍ  memorù  board®  Iô  ió �
responsiblå for:

     * Memory and I/O examination and modification.
     * Memory testing and comparison.
     * Execution of programs with or without breapoints set.
     * Examination and modification of CPU registers.
     * Disk bootstrap argument passing to disk driver.
     * Console ASCII-HEX & HEX-ASCII conversion.

ZBMC.*
     Thió  modulå containó thå Characteò I/Ï drivers®  Iô resideó �
iî  ROÍ  £  µ (F800..FFFFh© iî thå ROÍ  memorù  board®  Iô  ió �
responsiblå for:

     * Character I/O hardware & software initialization.
     * Logical-physical device conversion.
     * Single entry point support of driver function calls.
     * Function bypass entry points for Console, List & stdio.


ZBMK.*
     Thió modulå containó thå Disë I/Ï drivers® Iô resideó iî ROÍ �
£ 2 (F800..FFFFh© iî thå ROÍ memorù board®  Iô ió  responsiblå �
for:
     * Disk hardware & software initialization.
     * Disk boostrap.
     * Disk IOPB execution.


ZBMV.*
     Thió  modulå  containó  alì otheò  systeí  I/Ï  drivers®  Iô �
resideó  iî ROÍ £ 7 (F800..FFFFh© iî thå ROÍ memorù board®  Iô �
is responsible for:Š
     * Real time clock-calendar support.


.PAŠ.HE                         4.  ROM MODULES

     Thå  Monitoò  Systeí makeó uså oæ á seô oæ  ROMó  iî  Memorù �
board®  Alì  ROÍ  sharå  thå samå addresó rangå froí  F800è  thrõ �
FFFFh.

ROM  USE
0    Resident ROM, gets control on reset. Allways installed when
     the processor is executing outside the monitor system.
     (ZBMR)

±    RAM�

2    Disk drivers
     (ZBMK)

3    Debugger
     (ZBMD)

4    Character I/O drivers
     (M5ZC)

5    Spare

6    Spare

7    Additional I/O drivers
     (ZBMV)

.paŠ                      *** ENTRY POINTS ***

RESIDENT ROM:
Address   Function
F800      Cold start vector gets control upon Reset.

F803	  Return next System Console character
               EXIT - A= CHAR

F806      Execute Monitor Function (Same as RST 20H)
               ENTRY- Various, see section 5

F809      Send character to System Console device.
               ENTRY- C= Character to output

F80C      Return System Console output status
               EXIT - A= 0: Busy, /0: Ready

F80F      Send character to System List Device.
               ENTRY- C= Character to output

F812      Return System Console input status
               EXIT - A= 0: NOT READY, /0: CHAR READY

F815      Return Banked Memory contents
               ENTRY- E:HL= ADDRESS
               EXIT - A= DATA

F818      Store Banked Memory Contents
               ENTRY- E:HL= ADDRESS
                      C= DATA

F81B      Select 64K Memory Bank for execution
          **** WARNING! Stack must be in Common RAM! ****
               ENTRY- C= BANK #
               EXIT - A= BANK # ON ENTRY

F81Å      Seô Sourcå anä Destinatioî Bankó foò Blocë Movå function
               ENTRY- B= SOURCE BANK #
                      C= DESTINATION BANK #

F821      Move data from Source bank to destination bank
               ENTRY- HL= SOURCE PTR
                      DE= DESTINATION PTR
                      BC= BYTE COUNT

F824      Execute program in another Bank
               ENTRY- E:HL= ADDRESS TO EXECUTE
               EXIT - Whatever the called program returns

F827      Return System List device output status
               EXIT - A= 0: BUSY, /0: READY

F82Á      Reserveä foò internaì Debuggeò prograí breakpoinô entry
ŠF82D      Reserved for internal Debugger program execution support

F830      Restart Error

F833      Display character string on the System Console
          The last character must have Bit 7 set.
               ENTRY- HL= Character string pointer

F836      

F839      

F83C      

.PAŠCHARACTER ROM:
ADDRESS   FUNCTION

2000      Cold Start initialization

2006      Execute Monitor ROM function support
           (see Monitor ROM entry points)


.HE                         MONITOR DEVICES
.PAŠCharacter I/O

DEVICE    ASSIGNMENT
0         Naked Terminal board
1         Logical device #1
2         Logical device #2
.
.
.
15        Logical device #15

.paŠ.HE                5. MONITOR FUNCTION CALL FACILITY

     Thå  Systeí  Monitoò implementó á systeí  calì  facilitù  iî �
ordeò  tï  simplifù thå interfacå tï thå systeí  resources®  Thió �
wilì  allo÷  flexabilitù oæ implementinç thå  I/Ï  driveró  whilå �
preserving the software interface.

     Theså  functionó arå executeä bù placinç thå argumentó  intï �
thå   propeò registeró anä executinç á Restarô 20H.

Standard Arguments:
	A= Function #
	BC= Arg #1
	DE= Arg #2
	HL= Arg #3
	E:HL= Banked memory ptr

Standard Return Values:
	A= Byte
	HL= Word
	BC, DE= Additional values

     Return values:
NOTEº  Alì  functionó assumå alì registeró arå free®  Bå surå  tï �
savå anù datá prioò tï callinç thió function.

     Thå  Á  registeò  maù contaiî thå followinç  reserveä  erroò �
valueó oî return.

     -1:  Function not implemented error.
     -2:  Function argument error.


     Thå followinç pageó describå eacè functioî anä thå argumentó �
and returned values.
.he             *** Resident Functions descriptions ***
.paŠ
0:   RETURN SYSTEM MONITOR VERSION NUMBER
	  ENTRY- A= 0
	  EXIT - HL= BINARY VERSION # IN HUNDREDTHS (X.XX)

1º   RETURN BANKED MEMORY DATA.
     Unbankeä systemó ignorå E.
          Entry- A= 1
                 E:HÌ= Address ptr
          Exit - A= Data

2º   SET BANKED MEMORY DATA
     Unbanked systems ignore E.
          Entry- A= 2
                 Ã= Data
                 E:HL= Address ptr

3:   EXECUTE A PROCEDURE IN ANOTHER BANK
          Entry- A= 3
                 E:HL= Procedure address

4º   SELECT MEMORY BANKS FOR BANKED MEMORY BLOCK MOVE
          Entry- A= 4
                 Â= Source bank bank number
                 C= Destination bank number.

5º   PERFORM THE INTRABANK BLOCK MOVE
          Entry- A= 5
                 HL½ Sourcå pointer
                 DÅ= Destinatioî pointer
                 BÃ= Bytå counô tï move.

6:   SELECT A NEW BUS PROCESSOR (SS100)
          Entry- A= 6
                 C= Processor number {0,..7}

7:   RETURN CURRENTLY SELECTED BANK NUMBER
          Entry- A= 7
          Exit - A= Bank number

8:   Reserved for internal debugger function
          Entry- A= 8

9:   Select Bank for execution
          Entry- A= 9
                 C= Bank #

.he             *** Debugger Function Descriptions ***
.paŠ16:  RETURN DEBUGGER VERSION NUMBER
	  ENTRY- A= 10H
	  EXIT - HL= BINARY VERSION # IN HUNDREDTHS (X.XX)

17:  EXECUTE DEBUGGER
          ENTRY- A= 11H

18:  RESERVED FOR INTERNAL SYSTEM

19:  DISPLAY HEX NIBBLE ON THE SYSTEM CONSOLE.
          Entry- A= 13H
                 C<3..0>= nibble

20:  DISPLAY HEX BYTE ON THE SYSTEM CONSOLE.
          Entry- A= 14H
                 C= Byte

21:  DISPLAY HEX WORD ON THE SYSTEM CONSOLE.
          Entry- A= 15H
                 HL= Word

22º  DISPLAY HEX ADDRESS ON SYSTEM CONSOLE.
     Thió  functioî  ió  useä iî Bankeä memorù  systems®  Iæ  thå �
     systeí ió noô banked¬ theî iô ió redundanô witè functioî #3.
          Entry- A= 16H
                 E:HÌ= Address

23:  Display text on System Console
          Entry- A= 17H
                 HL= Ptr to Bit-7 terminated text

.he          *** Character I/O Device Driver Functions ***
.paŠ32:  RETURN CHAR DEVICE DRIVER VERSION #
          ENTRY-    A= 20H
          EXIT -    HL= Binary version # in hundredths (X.XX)

33:  EXECUTE CHAR DEVICE DRIVER FUNCTION
          ENTRY-    A= 21H
                    B= Device # {0..15}
                    C= Sub-function:
                         0: NOP (Can be used to test device
                                   presence)
                         1: Initialize device
                         2: Execute self test
                              EXIT- A= 0: Ok, /0: error code
                         3: Return device data
                              EXIT- L= Mode bits:
                                        0: Input device
                                        1: Output device
                                        2: Baud rate enabled
                                        3: XON/OFF Ok
                                        4: XON/OFF enabled
                                    H= Baud rate index
                         4: Set device data
                              ENTRY- E= Mode bits
                                     D= Baud rate index
                         5: Return Baud rate
                              EXIT - L= Baud rate index
                         6: Set Baud rate
                              ENTRY- E= Baud rate index

          EXIT -    A= -2: Device not present
                       -3: Argument error

34:  SPARE
          ENTRY-    A= 22H
          EXIT -    A= -1

35:  SET STANDARD DEVICE
          ENTRY-    A= 23H
                    B= Device # to set to {0..15}
                    C= Standard device to set
                         0: System console
                         1: System list
                         2: System AUX
                         3: System AUX2
          EXIT -    A= 0: Ok
                       -2: Illegal device
                       -3º Illegaì argumenô
                              (Stä devicå noô exist)
                    L= Device # on entry

36:  RETURN STANDARD AUX INPUT STATUS
          ENTRY- A= 24H
          EXIT - A= 0: NOT READY, /0: CHAR READY

37:  RETURN NEXT STANDARD AUX CHARŠ          ENTRY- A= 25H
          EXIT - A= CHAR

38:  RETURN STANDARD AUX OUTPUT STATUS
          ENTRY- A= 26H
          EXIT - A= 0: BUSY, /0: READY

39:  SEND CHAR TO STANDARD AUX OUTPUT
          ENTRY- A= 27H
                 C= CHAR

40:  RETURN STANDARD CONSOLE INPUT STATUS
          ENTRY- A= 28H
          EXIT - A= 0: NOT READY, /0: CHAR READY

41:  RETURN NEXT STANDARD CONSOLE CHAR
          ENTRY- A= 29H
          EXIT - A= CHAR

42:  RETURN STANDARD CONSOLE OUTPUT STATUS
          ENTRY- A= 2AH
          EXIT - A= 0: BUSY, /0: READY

43:  SEND CHAR TO STANDARD CONSOLE OUTPUT
          ENTRY- A= 2BH
                 C= CHAR

44:  RETURN STANDARD LIST DEVICE OUTPUT STATUS
          ENTRY- A= 2CH
          EXIT - A= 0: Busy, /0: Ready

45:  SEND CHAR TO STANDARD LIST DEVICE OUTPUT
          ENTRY- A= 2DH
                 C= Char

46:  RETURN STANDARD AUX2 INPUT STATUS
          ENTRY- A= 2EH
          EXIT - A= 0: NOT READY, /0: CHAR READY

47:  RETURN NEXT STANDARD AUX2 CHAR
          ENTRY- A= 2FH
          EXIT - A= CHAR

48:  RETURN STANDARD AUX2 OUTPUT STATUS
          ENTRY- A= 30H
          EXIT - A= 0: BUSY, /0: READY

49:  SEND CHAR TO STANDARD AUX2 OUTPUT
          ENTRY- A= 31H
                 C= CHAR


.HE                *** Disk I/O Driver Functions ***
.paŠ64:  RETURN DISK DRIVER VERSION #
          ENTRY-    A= 40H
          EXIT -    HL= Binary version # in hundredths (X.XX)

65:  BOOT DISK
          ENTRY-    A= 41H
                    BC= Physical drive #
                         Bit       Definition
                         2..0=     0
                         3=        0
                         7..4=     Drive #
                         15..8=    Controller #
          EXIT -    Error, will not return if successful

66:  TEST IOPB.PBSTATO FOR ERROR AND DUMP IOPB IF TRUE
          ENTRY-    A= 42H
                    E:HL= IOPB Ptr
          EXIT -    A= 0: NO ERROR, /0: ERROR CODE

67:  DISPLAY IOPB ERROR DATA
          ENTRY-    A= 43H
                    E:HL= IOPB Ptr
          EXIT -    A= 0: NO ERROR, /0: ERROR CODE

68:  EXECUTE IOPB
          ENTRY-    A= 44H
                    E:HL= IOPB Ptr
          EXIT -    A= 0: NO ERRORS, /0: ERROR CODE


.he	*** Miscellaneous I/O Driver Functions ***
.paŠ80:  RETURN MISCELLANEOUS DRIVER VERSION
          ENTRY-    A= 50H
          EXIT -    HL= Binary version # in hundredths (X.XX)

81:  SET CLOCK CALENDAR DATA
          ENTRY-    A= 51H
                    B= Day of month {1..31}
                    D= Month {1..12}
                    E= Year {0..99}
                    L= Day of week {0:Sun, 1:Mon,..6:Sat}

82:  SET CLOCK TIME DATA
          ENTRY-    A= 52H
                    B= Seconds {0..59}
                    D= Minutes {0..59}
                    E= Hours {0..23}

83:  RETURN CLOCK CALENDAR DATA
          ENTRY-    A= 53H
          EXIT -    A= Day
                    B= Month
                    C= Year
                    L= Day of week (0= Sunday, 1= Monday..)

84:  RETURN CLOCK TIME DATA
          ENTRY-    A= 54H
          EXIT -    A= Seconds
                    B= Minutes
                    C= Hours

85:  RETURN CLOCK REGISTER DATA
          ENTRY-    A= 55H
                    C= Register #
          EXIT -    A= Data from clock register

86:  WAIT FOR CLOCK TO CHANGE. DOES NOT RETURN UNTIL CLOCK SECONDS CHANGE.
          ENTRY-    A= 56H
          EXIT -    A= 0: OK
                       /0: Board not present

87:  SPARE
          ENTRY-    A= 57H
          EXIT -    A= -1

88:  STOP CLOCK
          ENTRY-    A= 58H

89:  START CLOCK
          ENTRY-    A= 59H

.HE                    *** Monitor Commands ***
.PAŠ     Thå Monitoò commandó musô conforí tï á specifiã format®  Thå �
general form is:

                           -Ca1 a2 a3

wherå  Ã  ió thå commanä characteò anä a1-a³ arå thå addresó  anä �
datá  entries¬  iæ any®  Thå essentiaì partó oæ á commanä arå  aó �
follows:

     Thå  Commanä Characterº  Thå monitoò ió controlleä  bù  one-�
characteò  commandó  entereä froí thå keyboarä iî reponså tï  thå �
monitoò  prompt¬  á  dasè (-)®  Nï spacå ió alloweä  betweeî  thå �
prompt and the command character.

     Addresó anä datá entriesº Thå generaì forí foò aî addresó ió �
á  fouò  digiô Heø number»  foò data¬  á twï  digiô  Heø  number® �
Leadinç zeroó neeä noô bå entered»  thå monitoò wilì supplù them® �
Nï  spacå ió alloweä betweeî thå commanä characteò anä thå  firsô �
addresó oò datá entry®  Subsequenô entrieó musô bå separateä bù á �
delimiter®  Thå  monitoò  lookó  aô onlù thå  lasô  fouò  addresó �
characteró oò lasô twï datá characteró beforå á delimiter®  Sï iæ �
yoõ  makå á mistakå whilå typinç aî entry¬  keeð typinç untiì thå �
lasô  fouò oò twï digitó arå correct®  Iî bankeä memorù  systems¬ �
thå banë numbeò ió delimiteä bù á coloî (:)¬  I.E®  bb:aaaa®  Thå �
addresó  entrù  ruleó  abovå applù tï  banë  numbeò  entries®  Iî �
addition¬  iæ á banë ió noô specified¬ theî thå lasô banë settinç �
is used by default.

     Delimitersº  Thå  Monitoò  recognizeó  threå  delimitersº  á �
carriagå  returî (CR)¬  á space¬  oò á comma®  Á carriagå  returî �
indicateó tï thå monitoò thaô thå currenô commanä ió completå anä �
shoulä  bå executed®  Eitheò á spacå oò commá caî marë thå enä oæ �
aî argumenô entry®  Iî ouò commanä exampleó wå wilì generallù uså �
á  spacå aó á delimiter¬  unlesó á commá makeó thå  commanä  forí �
clearer® Pleaså note¬ however¬ thaô yoõ caî uså thå spacå anä thå �
commá interchangeably® Iî certaiî commandó á spacå oò á commá caî �
alsï  bå interchangeä witè á carriagå return®  Theså arå commandó �
foò  whicè  thå Monitoò expectó á fixeä numbeò  oæ  entrieó  (anä �
hence delimiters) following the command character.

     Thå  followinç  commandó  tï  displaù thå  blocë  oæ  memorù �
120FFBè  tï 12100Aè arå alì equivalent®  Althougè thå spacinç  ió �
noô forí free¬  somå varietù iî thå commanä forí ió allowed® Notå �
thaô  thå  displaù  commanä requireó twï  anä  onlù  twï  addresó �
arguments¬  sï  thaô thå lasô delimiteò caî bå á commá oò á spacå �
as well as a carriage return.

                       -D12:0FFB 100A[CR]
                       -D0FFB 100A[CR]  (After 12: first used)
                       -DFFB,100A,
                       -DFFB,100A[CR]
                       -DFFB 100A[space]
                       -D0EF0FFB,100A[space]
                       -DFFB0012:FFB,100A[CR]
ŠCOMMAND DESCRIPTION


Boot Disk (B)

     Thió commanä allowó á disë operatinç systeí tï bå loadeä anä �
executed if loaded properly. The general form of the command is

                             B<arg>

where <arg> is the physical disk drive number.


Checksum Memory (C)

     Checksuí  memorù  displayó thå totaì positivå  anä  negativå �
checksuí oæ á rangå oæ memorù contents®  Thå generaì forí oæ  thå �
command is

                 C<start address> <last address>

where <start address> is the 1st location to checksum,
      <lasô  address¾  ió  thå lasô addresó  tï  checksum®  Afteò �
addinç thå datá byteó oæ alì thå memorù locationó  together¬  thå �
monitor displays the results as

                            pppp-nnnn

wherå  pppð  ió  thå  positivå checksuí valuå  anä  nnnî  ió  thå �
negative checksum value (negated pppp).


Display (D)
     Thió  commanä  allowó  yoõ  tï displaù  thå  contentó  oæ  á �
specified block of memory. The general form for the command is

                 D<start address> <last address>

wherå  <starô address¾ ió thå firsô bytå oæ blocë tï bå displayeä �
and <last address> is the last byte of the block to be displayed.

     Thå  resultinç displaù divideó thå memorù intï 1¶ byteó  peò �
line®  Eacè linå startó witè thå addresó oæ thå firsô bytå iî thå �
line¬  followeä  bù thå datá iî heø anä theiò ASCIÉ  equivalents® �
Thå contentó oæ locationó havinç thå samå lasô heø digiô iî theiò �
addresó arå aligneä vertically® Periodó represenô  datá foò whicè �
therå arå nï ASCIÉ equivalents®  Aó thå outpuô filló thå  screen¬ �
iô  wilì automaticallù scrolì up®  Tï freezå thå display¬  typå á �
control-Ó  (presó CTRÌ anä Ó keyó together)®  Tï starô iô  again¬ �
presó anù keù oî thå keyboard® Shoulä yoõ wisè tï escapå froí thå �
displaù  mode¬  pressinç  anù keù buô control-Ó  wilì  aborô  thå �
command and return to the monitor command entry mode.


ŠFill (F)

     Thå filì commanä allowó yoõ tï filì á blocë oæ memorù witè á �
specified constant. The general command form is

          F<start address> <last address> <fill value>

wherå  <starô address¾ ió thå firsô locatioî oæ thå memorù  blocë �
tï  bå filled¬  <lasô address¾ ió thå lasô addresó oæ thå  memorù �
blocë  tï  bå  filled¬  anä  <filì  value¾  ió  thå  constanô  iî �
hexadecimal.

EXAMPLE
     Entering
                        -F12:10AA 10BB 1

filló  thå memorù blocë 1210AAè througè 1210BBè witè thå constanô �
1.



Goto (G)

     Thå  Ç  commanä  allowó yoõ tï  transfeò  controì  froí  thå �
monitoò  tï anotheò program®  Iô allowó yoõ tï specifù thå  entrù �
addresó  anä  tï seô uð tï twï breakpointó foò returninç  controì �
tï  thå monitor®  Wheî thå monitoò encounteró  á  breakpoint¬  iô �
saveó  thå  contentó  oæ  thå  Z-8°  registeró  iî  thå  system'ó �
temporarù  storagå  anä displayó aî asterisë (*© followeä bù  thå �
nexô  addresó  iî thå program®  Iô theî returnó  tï  thå  monitoò �
commanä  modå witè thå prompt®  Yoõ caî uså thå Examinå  Registeò �
commanä  (X©  aô  thió  timå  tï  examinå  oò  changå  thå  saveä �
registers.

     The general form for the G command is

          G<start address>,<breakpoint 1>,<breakpoint 2

wherå  <starô address¾ ió thå entrù address¬  anä <breakpoinô  1¾ �
anä  <breakpoinô 2© arå thå addresseó oæ thå  breakpoints®  Therå �
arå manù alloweä variationó oî thió command¬ however¬ whicè makeó �
iô  á  powerfuì anä convenienô command®  Yoõ havå thå  optioî  oæ �
establishinç 0¬ 1¬ oò ² breakpointsº simplù enteò á [CRÝ wheî yoõ �
havå establisheä thå numbeò oæ breakpointó yoõ wish® Iæ yoõ enteò �
thå  maximum¬  two¬  á delimiteò (commá oò space© ió alì thaô  ió �
necessary to begin command execution.

     Yoõ  maù  alsï  begiî  executioî oæ thå prograí  aô  thå  PÃ �
addresó saveä iî thå registeò storagå area®  Thuó yoõ caî  returî �
controì  tï  thå  addresó  wherå  thå  prograí  stoppeä  wheî  iô �
encountereä  á breakpoint¬  oò tï thå addresó yoõ havå loadeä  iî �
thå saveä PÃ registeò througè thå Examinå Registeò command®  Notå �
thaô  sincå  alì breakpointó arå cleareä wheî anù  breakpoinô  ió �
encountered¬   yoõ   musô   specifù  oò  respecifù  anù   desireä �
breakpointó iî thå commanä iæ needed® Thå forí oæ thå commanä foò �Štransferring program control to the address in the PC register is

                             -G[CR]
                               or
                -G,<breakpoint 1>,<breakpoint 2>

     Therå arå twï morå pointó reguardinç breakpointó thaô  oughô �
tï  bå  mentioned®  Becauså breakpointó arå implementeä  usinç  á �
restarô  instructioî  op-codå  inserteä intï thå  prograí  tï  bå �
executed¬  breakpointó  caî  onlù  bå useä foò programó  iî  RAM® �
Breakpointó iî ROÍ wilì noô work® Additionally¬ á breakpoinô musô �
bå  useä  iî  placå oæ á valiä CPÕ  instructioî  op-codå  iî  thå �
program®  Iæ iô ió specifieä iî á operanä oò datá field¬  iô wilì �
not be executed.



Input (I)

     Thió generaì purposå inpuô commanä allowó yoõ tï reaä á datá �
byte from any input port. The general form of this command is

                         I<port address>

wherå <porô address¾ ió thå I/Ï porô addresó iî hex®  Thå monitoò �
will respond by printing the data byte in binary



Display clock/calendar data (K)

     Thió commanä allowó thå displaù oæ thå systeí clock-calendaò �
information. The form of this command is

                                K

After entry, the monitor displays the data in the form

                     hh:mm:ss  MM DD YY  ww

wherå hè ió thå timå iî houró (2´ houò format)¬ mí ió thå timå iî �
minutes¬  só ió thå timå iî seconds¬  MÍ ió thå month¬  DÄ ió thå �
date¬  YÙ ió thå year¬  anä w÷ ió thå daù oæ week® Alì datá ió iî �
hex.



Log on disk (L)

     Thió commanä allowó yoõ tï perforí thå disë logoî  function® �
Thió  musô bå performeä prioò tï anù reaä oò writå  commands®  Iô �
setó uð disë controlleò disë formaô tableó needeä tï perforí reaä �
& write operations. The general form of the command is

                L<address> <drive:track> <sector>Š
wherå  <address¾  ió  thå  addresó tï puô disë  IÄ  sectoò  data¬ �
<drive:track¾  arå  thå  physicaì drivå numbeò anä  tracë  oæ  IÄ �
sector, and <sector> is the sector # of ID sector.


Move (M)
     Thå  Í commanä moveó (Copies© á blocë oæ datá tï á specifieä �
address. The general form of the command is

     M<start address> <last address> <new address>

wherå <starô address¾ anä <lasô address¾ arå thå addresseó oæ thå �
firsô anä lasô byteó oæ thå memorù blocë anä <ne÷ address¾ ió thå �
destinatioî address.

     Wheî  usinç  thió  command¬  bå carefuì noô  tï  locatå  thå �
destinatioî addresó withiî thå sourcå block®  Sincå thå blocë  ió �
moveä  byte-by-byte¬  startinç  witè  thå bytå  witè  thå  lowesô �
address¬  thå datá beinç transferreä wilì writå oveò thå originaì �
contentó  oæ  thå  sectioî oæ thå sourcå blocë thaô  followó  thå �
destination address. This will be corrected in a future release.


Output (O)
     Thió  generaì purposå outpuô commanä allowó yoõ tï outpuô  á �
datá byte to any output port. Enter

                     O<port address> <data>

wherå  <porô address¾ ió thå I/Ï porô addresó anä <data¾  ió  thå �
datá in hex.


Read (R)
     Thió  commanä  allowó  yoõ tï reaä  disë  sectoò  data®  Thå �
general form of the command is

                R<address> <drive:track> <sector>

wherå   <address¾  ió  thå  addresó  tï  puô  thå  sectoò   data¬ �
<drive:track¾ ió thå logicaì drivå numbeò anä tracë numbeò oæ thå �
sectoò, and <sector¾ is the sectoò number to be read.


Substitute (S)
     Thå substitutå commanä allowó yoõ tï examinå thå contentó oæ �
á specifiã memorù locatioî anä alteò iô iæ yoõ desire®  Begiî thå �
S command by entering

                           S<address>

wherå <address¾ ió thå addresó oæ thå memorù locatioî yoõ wisè tï �
examine®  Thå  monitoò  wilì immediatlù responä witè thå  currenô �
data contents followed by a prompt:Š                       -<address>,<data>-

Iæ  yoõ  wisè  tï  leavå  thå  datá  unchanged¬  simplù  enteò  á �
delimiter® Iæ thå delimiteò ió á spacå oò comma¬ thå monitoò wilì �
responä witè thå contentó oæ thå nexô consecutivå memorù locatioî �
anä anotheò prompt®  Iæ iô ió á carriagå return¬  thå commanä  ió �
terminateä  anä  thå  monitoò  respondó witè  thå  commanä  entrù �
prompt®  Shoulä  yoõ wisè tï changå thå data¬  enteò thå  desireä �
datá  followeä bù á delimiterº  á carriagå returî iæ yoõ wanô  tï �
terminatå  thå commanä oò á spacå oò commá iæ yoõ wisè tï  revie÷ �
thå nexô memorù location® Yoõ caî causå thå commanä tï bacë uð tï �
thå  previouó locatioî bù enterinç á Linå Feeä (CTRL-J)®  Yoõ caî �
continuå  examininç anä changinç memorù byte-by-bytå iî thió  waù �
aó lonç aó yoõ wish®  Tï makå iô easieò foò yoõ tï keeð tracë  oæ �
wherå  yoõ  are¬  oî everù 8-bytå boundarù (thaô is¬  aî  addresó �
endinç  iî ° oò 8© thå monitoò wilì starô oî á ne÷ linå witè  thå �
addresó anä datá again.



Test (T)
     Thå tesô commanä provideó á quicë waù tï tesô RAÍ memorù foò �
harä  datá  biô failureó withouô destroyinç thå contentó  oæ  thå �
RAM. To test a block of memory for bit failures, enter

                 T<start address> <last address>

wherå <starô address¾ anä <lasô address¾ arå thå addresseó oæ thå �
firsô anä lasô byteó iî thå block¬ respectively® Thå monitoò wilì �
responä bù displayinç thå addresó oæ anù bytå iî error¬  followeä �
bù aî 8-biô binarù representatioî oæ thå bitó iî error¬  iî whicè �
a 1 indicates a bit in error. For example, the display

                          F038 00010000

woulä indicatå thaô biô ´ oæ thå bytå iî memorù locatioî F03¸  ió �
iî  error®  Iæ yoõ wisè tï freezå thå displaù typå á  CTRL-S®  Tï �
starô iô again¬ presó anù key® Pressinç anù keù whilå thå commanä �
is executing will abort the command.



Update clock data (U)
     Thió  commanä  allowó yoõ tï seô thå systeí  clock-calendar® �
The general form of the command is

 U<hours>:<Minutes¾ <Month>:<Daù oæ month¾ <Year>:<Daù oæ week>

wherå  <Hours¾ ió thå timå houró {0..17}¬  <Minutes¾ ió thå  timå �
minuteó  {0..3B}¬  <Month¾ ió thå montè numbeò  {1..C}¬  <Daù  oæ �
month¾ ió thå datå {1..1F}¬  <Year¾ ió thå lasô twï digitó oæ thå �
yeaò  {0..63}¬  anä  <Daù  oæ  week¾ ió thå  daù  numbeò  {0:Sun¬ �
1:Mon,..6:Sat}®  NOTEº  alì numberó currentlù musô bå entereä  iî �
hex.
Š
Verify (V)
     Yoõ  caî  uså thå Ö commanä tï comparå twï blockó oæ  memorù �
and verify that they are the same. Type

       V<start address> <last address> <2nd start address>

wherå <starô address¾ anä <lasô address¾ arå thå addresseó oæ thå �
firsô  anä lasô bytå oæ thå sourcå blocë anä <2nä starô  address¾ �
ió thå startinç addresó oæ thå blocë tï bå verified®  Shoulä  thå �
twï blockó match¬ thå monitoò wilì returî witè thå prompt® Shoulä �
twï  correspondinç  byteó differ¬  thå monitoò wilì  displaù  thå �
sourcå  addresó anä itó contentó iî hex¬  followeä bù á dasè  (-© �
anä  thå contentó oæ thå correspondinç addresó oæ thå blocë beinç �
verified® Durinç thå executioî oæ thå command¬ thå displaù caî bå �
frozeî  oò controì returneä tï thå monitoò aó describeä  foò  thå �
Test command.


Write disk sector data (W)
     Thió  commanä allowó yoõ tï writå datá iî memorù tï á sectoò �
on a disk. The general form of the command is

                W<address> <drive:track> <sector>

wherå  <address¾  ió thå memorù addresó tï geô  thå  sectoò  datá �
from¬  <drive:track¾ ió thå logicaì drivå numbeò anä tracë numbeò �
oæ the sector, and <sector> is the sector number to write to.


Examine (X)
     Thå  Ø  commanä  ió  á  verù usefuì  commanä  wheî  useä  iî �
conjunction with the G command's breakpoint facilities. Entering

               -X<Carriage return, space or comma>

causeó  thå  CPÕ registeò imageó currentlù storeä iî  RAÍ  tï  bå �
displayeä  foò  examination®  Theså  registeró arå thå  maiî  anä �
alternatå   accumulatoò  anä  generaì  purposå   registers¬   thå �
Interrupô  registeò  (I)¬  thå Prograí  Counteò  (P)¬  thå  Stacë �
Pointeò registeò (S)¬  thå twï Indeø registeró (Ø anä Y)¬ anä thå �
Refresè  registeò (R)®  Iî addition¬  thå contentó oæ thå  memorù �
locationó  addresseä bù thå maiî anä alternatå È anä Ì  registeró �
arå  alsï displayeä (Í anä M')®  Foò bankeä memorù  systems¬  thå �
banë  numbeò  selecteä  bù thå Ç commanä prioò tï  executinç  thå �
addresó  aô thå Ð registeò ió displayeä (K)®  Thå  registeró  arå �
displayed in the following format

          A-xx B-xx C-xx D-xx E-xx F-xx H-xx L-xx
          M-xx P-xxxx S-xxxx I-xx
          A'-xx B'-xx C'-xx D'-xx E'-xx F'-xx H'-xx L'-xx
          M'-xx X-xxxx Y-xxxx R-xx
          K-xx

wherå  xø representó á two-digiô heø bytå anä xxxø  representó  á �Šfour-digiô heø address.

     To examine or alter the contents of one register, enter

              -Xr<Carriage return, space or comma>
                               or
              -X'r<Carriage return, space or comma>

wherå ò ió á maiî registeò anä 'ò ió aî alternatå register® (Notå �
thaô iæ yoõ wisè tï examinå thå X¬  Y¬  oò Ò registers¬  yoõ musô �
prefacå thå registeò characteò witè thå primå characteò (').© Thå �
monitor will display the contents of the register and a prompt:

                             -Xr,Dh-

Aó  iî  thå  substitutå memorù command¬  yoõ havå thå  optioî  oæ �
changinç  thå  registeò  valuå  (enterinç  thå  desireä  contentó �
followeä  bù  á  delimiter© oò  leavinç  thå  contentó  unchangeä �
(enterinç á delimiteò witè nï data)® Á carriagå returî terminateó �
thå  command»  á spacå otò commá causeó thå contentó oæ thå  nexô �
registeò tï bå displayed®  Notå thaô changinç thå contentó oæ thå �
È  anä Ì registeró changeó thå address»  iæ yoõ wisè tï alteò thå �
contents of the memory location, alter the M register



GRH/zbm-122.doc