## Slide 1: HP ProLiant DL160 Generation 5 (G5)
14 January 2008 Announcement
HP Industry Standard Servers
Notes: © Copyright 1996, 1997–2008 Hewlett-Packard Development Company, L.P.
The information contained in this presentation is proprietary to Hewlett-Packard Company and is offered in confidence, subject to the terms and conditions of a Confidential Disclosure Agreement (CDA).
HP requires customers and partners to have signed a CDA in order to view this training. The information contained in this training is HP Confidential, but will become HP Restricted after announcement.
HP does not warrant or represent that it will introduce any product to which the information relates. The information contained herein is subject to change without notice. HP makes no warranties regarding the accuracy of this information. The only warranties for HP products and services are set forth in the express warranty statements accompanying such products and services. Nothing herein should be construed as constituting an additional warranty. HP shall not be liable for technical or editorial errors or omissions contained herein.
This is an HP copyrighted work that may not be reproduced without the written permission of HP. You may not use these materials to deliver training to any person outside of your organization without the written permission of HP.
Microsoft and Windows are U.S. registered trademarks of Microsoft Corporation.
Intel and Pentium are trademarks or registered trademarks of Intel Corporation in the U.S. and other countries.
New Product Introduction HP Restricted

## Slide 2: What is announcing
HP ProLiant DL160 Generation 5 (G5)
The HP ProLiant DL160 Generation 5 platform is taking the place of the HP ProLiant DL140 server
Key new features or capabilities
Supports up to two Intel Xeon™ processors 5400 Sequence Harpertown Quad-Core 2 x6MB Level 2 cache 5200 Sequence Wolfdale Dual-Core 1 x6MB Level 2 cache 1066/1333/1600 MHz front side bus Intel 5400 chipset More storage capacity
Availability: 14 January 2008
DL160 G5 on HP.com:
http://h10010.www1.hp.com/wwpc/us/en/en/WF04a/15351-15351-3328412-241644-3328421.html
Access panel
Up to two (2) Intel Xeon™ processors
Eight (8) DIMM memory slots
650W power supply
System fans
Optional optical drive
Two (2) USB ports
Power on/off & system LEDs
Two (2) 3.5” hard drive bays
Two (2) 3.5” hard drive bays
Expansion Slots
1
2
3
4
5
6
7
8
9
10
11
Notes: What is announcing
    The DL160 G5 server is an Intel-based, 1U form factor, rack-mount server with up to two Intel Xeon™ 5000 sequence quad-core processors.
  Why this product now?
    The DL160 G5 server is the next generation platform of the DL140. There will no longer be a DL140 G4 the DL160 is taking its place. The DL160 offers Intel’s latest processors, Intel’s latest chipset and more storage capacity then the DL140.
      Support for Intel’s latest processors, with improved frequencies, Level 2 cache, and front side bus (FSB)
      Target customer include: high performance computing (HPC), web farms, large data centers, small and medium business (SMB)
      HP is the first tier one vendor to have four drives in 1U form factor
  What’s new
    Maximum performance at minimum cost
    On the day of announcement, HP will announce these new features and functionality:
      Latest Intel Xeon™ Processors — Support for the new 5400 sequence quad-core and 5200 sequence dual-core processors.
      FSB speed — 1600MHz FSB options now available.
      Intel’s 5400 chipset — Optimized for HPC and streaming workloads.
      Storage capacity — Now supports up to four 3.5” HDD bays (SAS or SATA).
  Warranty
    The DL160 G5 offers a World-wide limited warranty that includes 1 year parts, 1 year labor, 1 year on-site support. A variety of upgrades are available through HP Care Packs. For more information please visit:
    http://h18004.www1.hp.com/products/servers/platforms/warranty/index.html

## Slide 3: Product and technology overview
Servers provide data to users on a network and designed for specific markets, needs, and applications
  Data, printers, and modems are shared
  Applications, such as email, are shared
  Internet connectivity is shared
  Network security is important
  Large amounts of data must be stored and processed
  The system must operate 24 hours a day, 7 days a week
DL160 G5 server
  Entry-level 2P server designed for high-performance cluster computing
  Maximum performance in a small footprint for dense rack-mount environments
  Entry-level for small medium businesses (SMB)
  Companies with remote locations can take advantage of remote management
  Affordable price
Notes: <header>
<date/time>
Product and technology overview
    Servers provide data to users on a network. Servers are designed for specific markets, needs, and applications. They can be used where:
      Data, printers, and modems are shared.
      Applications, such as email, are shared.
      Internet connectivity is shared.
      Network security is important.
      Large amounts of data must be stored and processed.
      The system must operate 24 hours a day, 7 days a week.
    Servers can be differentiated from desktop computers based on hardware and technology:
      Processors — Servers support multiple processors, whereas desktop computers support only one processor.
      Memory — Servers support significantly larger amounts of memory than desktop computers.
      Storage — Servers are designed for more external and internal storage. Desktop computers are not designed for large amounts of either type of storage.
      System architecture — Servers are designed to minimize bottlenecks that can be encountered when multiple users access a server simultaneously.
      Video and sound — Desktop computers typically contain more advanced video and sound technologies than servers because they are more often used for running and viewing graphic-intensive games and programs.
    Secondly, the DL160 G5 was specifically designed for and rigorously tested with server applications in demanding server configurations. This testing cycle ensures optimal performance and dependability when deployed as a server. Finally, the DL160 G5 is packaged in an ergonomic chassis that makes typical server hardware configuration changes simple. By not including expensive graphics or sound cards found in desktop PCs the DL160 G5 is able to offer true server functionality at an equivalent desktop PC price.

## Slide 4: Intel Xeon™ processors
  Support for up to two Intel Xeon™ processors
  Reliable, efficient, and have proven performance
  Built with Intel's 45nm technology and optimized for high bandwidth clusters and super computers
  45nm Enhanced Intel Core micro architecture delivers maximum performance with efficient power consumption
  Flexibility to match performance, power, and cost requirements with customer requirements
  Cost optimized, high-performance 1U rack mount x86 server
  Virtual Machine Device Queues (VMDq) sorts data through multiple queues resulting in efficient network processing
  Intel VT FlexPriority optimizes virtualization software efficiency by improving interrupt handling
  VT FlexMigration allows new and future Intel Xeon™ processor based systems to be added to the same resource pool
Notes: <header>
<date/time>
Intel Xeon™ processors
    HP ProLiant DL160 G5 Server Blade uses breakthrough performance, energy efficiency, and reliability of the Intel Xeon™ processor. Making it the ideal choice for all data demanding or standard enterprise infrastructure applications. Intel Xeon™ processors achieve this by using Intel 45nm technology:
      Intel 45nm high-k (Hi-k) metal gate silicon technology is the next-generation Intel Core Microarchitecture. With roughly twice the density of Intel 65nm technology
      Intel's 45nm packs about double the number of transistors into the same silicon space, more than 400 million transistors for dual-core processors and more than 800 million for quad-core
      Intel's 45nm technology enables great performance leaps, up to 50-percent larger L2 cache, and new levels of breakthrough energy efficiency
    Built for Virtualization
    Intel Xeon™ processor-based server platforms deliver incremental headroom and performance for two-processor general-purpose server, and can confidently consolidate applications onto fewer systems with fewer cooling challenges, giving you more performance per square foot.
      Platforms have integrated virtualization hardware support with Intel Virtualization Technology, which enables more efficient virtualization solutions, Intel VT works by hardware assisting your virtualization environment
    Delivering Compelling Performance Per Watt
    Intel has used its new 45nm process technology to extend its Intel Core microarchitecture and deliver even higher levels of performance and density with fewer cooling challenges. The new 45nm Enhanced Intel Core microarchitecture delivers more performance in the same platforms and at the same power consumption, giving IT the flexibility to match performance, power and cost requirements with unique requirements and delivering business and IT advantages beyond just pure performance

## Slide 5: Intel 5400 chipset
  Optimized for HPC and streaming workloads
  Improved Front side bus (FSB) speed
    Support for 1066/1333/1600 MHz FSB
  The Dual Independent Bus provides independent point to point interconnects between each of the processors and the chipset
  Input output (I/O) support for
    PCI-Express x16 Gen2
    133 MHz PCI-X 64 bit
  Reliability, availability, and serviceability
    Error Correction Code (ECC)
    DIMM sparing and DIMM scrubbing
    Single Device Data Correction
Notes: <header>
<date/time>
Intel 5400 chipset
    The Intel 5400 chipset is bandwidth-enhanced for dual socket high performance applications. It provides support for faster processor, bus, and I/O speeds to enhance performance in demanding technical computing environments.
    The Intel 5400 chipset improves data movement across Quad-Core Intel Xeon™ processor 5400 and Dual-Core Intel Xeon™ processor 5200 series-based systems by increasing interconnect bandwidth, optimizing system bandwidth, increasing memory capacity, and improving network traffic processing while reducing I/O latency. These platform advancements help to match the improved performance provided by the Quad-Core Intel Xeon™ processor 5400 series.
      Dual Independent Bus — The Dual Independent Bus provides independent point-to-point interconnects between each of the processors and the chipset. Speeds up to 1600 MT/s.
      PCI-E I/O support — Serial I/O technology provides a direct connection between the MCH chipset and PCI Express component/adapters with bandwidth up to 48 GB/s on each PCI Express generation 2 x8 interface. PCI Express offers higher bandwidth, lower latency and fewer I/O bottlenecks than PCI-X.
      PCI-X I/O support — Optional component supports PCI/PCI-X performance and provides significant enhancements to platform flexibility. Supports two independent 64-bit, 133 MHz PCI-X segments and two Hot-Plug controllers (one per segment).
      Virtualization Technology — Enhancements to Intel Virtualization Technology performance that further speeds up virtual machine transition (entry/exit) times by an average of 25 to 75 percent.
      Advanced Platform — Features such as memory Error Correction Code (ECC), Intel x4 Single Device Data Correction (x4 SDDC), DIMM sparing and DIMM scrubbing for improved system reliability.

## Slide 6: Storage capacity
  Supports up to four
    3.5” Non-Hot plug serial ATA (SATA) 3.5"hard drives; or
    3.5” Hot-plug Serial Attached SCSI (SAS) or SATA hard drives
  Internal storage capacity of up to
    3TB, 4 x 750GB Hot Plug 3.5" SATA
    2TB, 4 x 500 Non-Hot Plug SATA
    1.2TB, 4 x 300GB Hot Plug 3.5" SAS
  Storage Controllers
    HP Embedded SATA RAID Controller on Non-Hot Plug SATA Models
    HP SC40Ge 4-Port Internal SAS HBA with RAID 0, 1 on Hot Plug SAS/SATA Models
    HP Smart Array E500 Controller
    HP Smart Array E200 Controller
    HP SC11Xe Host Bus Adapter
    HP SC44Ge Host Bus Adapter
Notes: <header>
<date/time>
Storage capacity
    HP beats the competition by being the 1st Tier-1 vendor with four 3.5” HDDs in 1U server form factor.
    Supports up to four
      3.5” Non-Hot plug serial ATA (SATA) 3.5"hard drives; or
      3.5” Hot-plug Serial Attached SCSI (SAS) or SATA hard drives
    Internal storage capacity of up to
      3TB, 4 x 750GB Hot Plug 3.5" SATA
      2TB, 4 x 500 Non-Hot Plug SATA
      1.2TB, 4 x 300GB Hot Plug 3.5" SAS
    Storage Controllers
      HP Embedded SATA RAID Controller on Non-Hot Plug SATA Models
      HP SC40Ge 4-Port Internal SAS HBA with RAID 0, 1 on Hot Plug SAS/SATA Models
      HP Smart Array E500 Controller
      HP Smart Array E200 Controller
      HP SC11Xe Host Bus Adapter
      HP SC44Ge Host Bus Adapter

## Slide 7: HP product family positioning
 | DL160 G5 | DL165 G5 | DL365 | DL140 G3
Processors | Up to two quad or dual core Intel Xeon™ processors | Up to two quad or dual core AMD Opteron processors | Up to two AMD Opteron processors | Up to two quad or dual core Intel Xeon™ processors
Form Factor | 1U | 1U | 1U | 1U
DIMM Slots | 8 | 8 | 8 | 8
Max Memory | 32GB (4GB DIMMs) | 32GB (4GB DIMMs) | 32GB (4GB DIMMS) | 32GB (4GB DIMMs)
Management | LO100 | LO100 | iLO2 | LO100i
Drive support | (4) 3.5” NHP/HP | (4) 3.5” NHP/HP | (6) SFF hot-plug | (2) 3.5” NHP/HP
PCI slots standard | (1) x16 PCI-E G2 (LP), (1) x16 PCI-E G2 (FL/FH) | (1) x4 elec. x8 mech. PCI-E (LP), (1) x16 PCI-E (FL/FH) | (1) x8 PCI-e FH/FL, (1) x8 PCI-e LP | (2) x8 PCI-E LP, (1) x4 and (2) x8 PCI-E
PCI Slots optional | (1) 133 MHz PCI-X 64 bit (LP), (1) 133 MHz PCI-X 64-bit (FL/FH) | LP Option: 133 MHz PCI-X or FH/FL option: HTX | 133MHz PCI-X (FL/FH) | (1) x16 and (1) x4 PCI-e or 133MHx PCI-X and (1) x8 PCI-E
NICs | (2) Gigabit | (2) Gigabit | (2) Multifunction Gigabit | (2) Gigabit
RPS option | No | No | Hot Plug RPS | No
Warranty | 1-1-1 | 1-1-1 | 3-3-3 | 1-1-1
Key: LFF = large form factor hard drives, LP = low profile slots, SFF = small form factor, FL/FH = full length/full height slots
Notes: <header>
<date/time>
HP product family positioning
    The DL160 G5 is an affordable 1U, Intel based, dual processor capable server with essential performance features designed for general purpose solutions and high performance computing environments. It is an exceptional value and is easy-to-own through industry standard tools and components.
    Target markets
      HPC
      SMB
      Web Farms
      Large data centers
    The new ProLiant DL160 G5 is designed for quality, performance, and flexible deployments to meet the needs of the HPC, SMB market, and corporate scale-out market segments.

## Slide 8: Customer opportunities Look for these customers
  Ideal for Web/Edge servers, network services such as domain/DNS/DHCP serving, basic file/print, or as an high performance computing (HPC) compute node
  Intel’s latest processor architecture delivers ultimate processor performance
  Customers transitioning to total cost of ownership (TCO) concept of costing
  Maximum performance in a small footprint for dense rack-mount environments
  Need for large amounts of local storage with dual processor performance
  Quad-core processing capability at an affordable price
Technology strategies: Delivering a low cost robust 2P system with Intel's latest processor architecture and additional features
Customer size: SMB and Midmarket
Business requirement: More emphasis on performance and energy efficiency
Target markets: HPC, scientific research, engineering, web serving, Web 2.0
Business requirement: Maximum server performance at prices that meet business’ budget needs
Notes: <header>
<date/time>
Customer opportunities
    For selling opportunities, look for customers with the following business challenges:
      Customer are looking for affordable pricing for a well-featured rack-optimized, 1U form-factor, 2P quad-core system.
        Customers transitioning to TCO concept of costing, looking for cost-optimized, high-performance 2P/1U rack-mount x86 server, and large amounts of local storage.
        Customer benefits: The DL160 G5 combines affordability, density, and manageability with the performance advantage of Intel processors. Intel Core microarchitecture delivers more performance in the same platforms and at the same power consumption achieving TCO and high performance. The DL160 G5 also supports four 3.5” SAS or SATA hard drives for up to 3TB of data storage. This allows maximum performance and storage all in a 1U small footprint for dense rack-mount environments.

## Slide 9: Use case scenario 1 — HPC cluster
Purposes include:
  Data centers
  Scientific research
  Engineering applications
  Transaction processing
Current challenges with HPC clusters:
  Infrastructure limitations
  Implementation and management
  Price/performance/efficiency
DL160 G5 solution:
  Maximum server performance with Intel’s latest Quad-Core technology
  1U small footprint for dense rack-mount environments
  High-efficiency memory, processors, and power supplies to maximize efficiency/watt & minimize TCO
  Lights-Out 100i gives IT remote management
Benefits:
  Fewer staff management hours
  More agile environment
  Efficient, powerful, reliable HPC clusters
Notes: <header>
<date/time>
Use case scenario 1 — HPC cluster
    The DL160 G5 is the ideal compute node for HPC Clusters. It offers maximum compute, high density, and essential management capability.
    Chassis/Form Factor
      1U, ~27” deep Chassis
      Standard 19” wide rack rails
      Four 3.5” HDD bays (SAS or SATA)*
      Optical drive bay
      High efficiency power supply option
    Manageability & Connectivity
      Embedded management
      Lights Out 100i (DP systems)
      TPM optional for MS BitLocker
      Dual 1Gb NICs
      Rear PS2, USB, video and serial ports
      PCI-Express X16 Gen2 (Intel)
    System capability
      Intel Xeon™ 5000 Model
      32GB DDR2 (8 slots)
      2 PCI-Express gen 2 standard (dual x16)
      Based upon Intel 5400 chipset:
      Optimized for HPC and streaming workloads
      Support for up to 1600MHz FSB Storage
    Storage
      SATA RAID 0,1
      Optional SAS/SATA RAID 0,1,5

## Slide 10: Use case scenario 2 — Remote management
Problem:
  Servers located in branch offices with no local server support employees or are located off site and require remote control capabilities
Current challenges:
  24x7 continuous remote control
  Cost effective remote management
  Reduce the need to physically visit or find onsite assistance to support
LO100i solution:
  Provides standards based remote control that is consistent with the overall remote management strategy
  KVM over IP for full remote graphical console capabilities
  Enables anytime access to system management information such as hardware health and event logs
Benefits:
  Simple and affordable remote management
Notes: <header>
<date/time>
Use case scenario 2 — Remote management
    HP Lights-Out 100 Remote Management, it is a cost-effective, entry level remote management solution for the ProLiant 100 series servers. It is intended to provide standards based remote control that is consistent with the overall strategy for ProLiant 100 series servers - simple and affordable computing.
    Lights Out 100 is based on the IPMI standard.
      IPMI is the abbreviation for Intelligent Platform Management Interface and is an Intel-driven, server management effort that delivers hardware management to the cost-sensitive server market.
    Lights-Out 100 Remote Management
      Basic, affordable, continuous remote control that comes in several flavors to complement the ProLiant 100 series that you see reflected in this slide:
    Whereas the ML series is suited for SMB environments and single-tier architectures you will see typically a requirement for the Lights Out 100 Standard or the Lights Out 100c which is a mezzanine card for tower servers.
      LO100i Standard is basic remote management via unsecured interfaces
      LO100c Card is remote management via unsecured interfaces
    Whereas the DL series is suited for HPC and HPTC environments, you will see typically customers choose to acquire Lights Out 100i Advanced or Select Packs.
      LO100i Advanced is a cost-effective, secure remote control complete w/ embedded KVM over IP
      LO100i Select is a essential, secure remote control with remote serial console
    Regardless of whether you choose Lights Out 100c or Lights Out 100i, you get control of your Power, KVM/serial consoles, USB storage and the ability to monitor system Health and logs

## Slide 11: Competition
 | HP ProLiant DL160 G5 | Dell PowerEdge SC1435
Processors | Up to two quad or dual core Intel Xeon™ processors | Up to two dual core AMD Opteron processors
Form Factor | 1U | 1U
DIMM Slots | 8 | 8
Max Memory | 32GB (4GB DIMMs) | 32GB (4GB DIMMs)
Drive support | Up to 4 drives (hot-plug or non-hot plug) 7.2K RPM SATA (160GB, 250GB, 500GB, 750GB) 15K RPM SAS (36GB, 72GB, 146GB, 300GB) | Up to 2 drives (hot-plug or non-hot plug) 7.2K RPM SATA (80GB, 160GB, 250GB, 500GB, 750GB) 10K RPM SAS (146GB, 300GB, 400GB) 15K RPM SAS (36GB, 73GB, 300GB)
RAID Controllers | RAID 0,1 with SC40Ge, RAID 5 with SA E200, P400, P800 | RAID 0,1 with SAS 5iR, RAID 5 with PERC 5i
Ports | 5 USB 2.0 (2F/1int/2R) | 4 USB 2.0 (2F/2R)
Redundant Power Supply | No redundant power supply, optional HE PSU | No redundant power supply, no HE PSU option
Graphics | Integrated 32MB SRAM video | ATI ES1000 controller with 16MB of SDRAM
PCI slots standard | (1) x16 PCI-E G2 (LP), (1) x16 PCI-E G2 (FL/FH) | 1 PCI-Express G1
PCI Slots optional | (1) 133 MHz PCI-X 64 bit (LP), (1) 133 MHz PCI-X 64-bit (FL/FH) | 133 MHz PCI-X (FL/FH)
NICs | (2) Gigabit | (2) Gigabit
Optical Storage | Optional | Optional
Notes: <header>
<date/time>
Competition
    HP offers the most comprehensive, density-optimized solutions for rack environments that are adaptable to a wide range of complex, growing multi-server environments.
    HP Overall Advantages
      The DL160 G5 offers up to four hard drives (hot-plug or non-hot plug) as compared to two on the Dell model.
      Optional HE PSU where the Dell does not.
      More PCI expansion options
      HP ships more servers than anyone.
      HP is #1 in total worldwide server revenue.
      HP leads the x86-64 Xeon™ EM64T based server market.
      HP continues to lead and gain in the worldwide Windows market.
      HP maintains the lead in the worldwide Linux market.
      HP leads in worldwide shipments in major operating systems.
      HP offers 65,000 service professionals with unmatched technical expertise in over 160 countries, including 28,000 Microsoft trained specialists, 5,200 Microsoft certified experts, 6,500 Linux experts, 5,000 Consultants on J2EE and .NET, 1,400 Cisco experts, and 3,000 SAP experts.
    Proven superior support over Dell
      Dell’s service programs lack global consistency.
      Dell support offerings are not constant across the Dell server lines – low end and high end products are not always eligible for the same service.
      Dell will provide support on “commodity” products, but does not develop expertise on complex products (such as high end storage arrays). Dell will outsource complex issues.
      Dell’s service competencies are Dell products only.
      Dell lacks support for multi-vendor complex environments.
      Dell can support the Wintel environment only.

## Slide 12: Resources

## Slide 13: Tools and resources
HP ProLiant DL160 on HP.com
  http://h10010.www1.hp.com/wwpc/us/en/en/WF04a/15351-15351-3328412-241644-3328421.html
Business Support Center
  http://h20000.www2.hp.com/bizsupport/TechSupport/Home.jsp?&lang=en&cc=us&prodTypeId=15351&prodSeriesId=3232017&lang=en&cc=us&y=0DL180&x=0
HP ProLiant Essentials management software
  http://www.hp.com/servers/proliantessentials
HP ProLiant options
  http://h18004.www1.hp.com/products/servers/platforms/options.html
HP Factory Express
  http://www.hp.com/go/factory-express
Worldwide limited warranty and technical support
  http://h18004.www1.hp.com/products/servers/platforms/warranty/index.html
HP Care Pack services
  http://www.hp.com/go/proliant/carepack
Notes: <header>
<date/time>
Tools and resources
    This slide includes helpful tools and resources available on the HP website.

## Slide 14: Regional product marketing contacts
Sales issues |  |  | Presales support issues | 
Product availability Special pricing Qualifying customers Order entry, configuration, or status issues |  |  | Technology or supported configuration questions Planning and deployment scenarios Infrastructure requirements | 
Region | Contact | Email |  | Location
US | Tim Golden | tim.golden@hp.com |  | Houston, US
Latin America | Carlos Cuina | carlos.cuina@hp.com |  | Houston, US
EMEA | Tony Bunn | tony.bunn@hp.com |  | Bracknell, GB
Asia Pacific | Naren Nuggehalli | naren@hp.com |  | Singapore, SG
Japan | Iekazu Okano | iekazu.okano@hp.com |  | Tokyo, JP
Notes: <header>
<date/time>
Regional product marketing contacts
    For any of the issues listed above, contact the product manager listed for your region.

## Slide 15
Notes: <header>
<date/time>

## Slide 16: Focus-Level

## Slide 17: External view (front)
Item | Description
1 | Optional optical drive
2 | USB port for easy access
3 | Common diagnostic panel across platforms for fast health status
4 | 1U rack form factor
5 | Four (4) SAS/SATA drive bays
6 | Power on/off switch
1
2
3
4
5
6
Notes: <header>
<date/time>
External view (front)
    This slide shows the external front view. For a complete description, refer to the user guide located at: http://www.hp.com/servers/proliant

## Slide 18: Order, configuration, and licensing rules
Configure-to-order (CTO) rules
  Step 1: Base Configuration
  Step 2: Choose Required Options
    Processors
    Memory
    Hard Drives
    Storage Controller
    Power supply
  Step 3: Choose Additional Options for Factory Integration
Factory Express rules
  HP Factory Express offers configuration, customization, integration and deployment services for HP servers and storage products. Customers can choose how their factory solutions are built, tested, integrated, shipped and deployed.
Helpful websites
  http://www.hp.com/servers/proliantessentials
  http://www.hp.com/servers/lights-out
  http://www.hp.com/products1/storage/compatibility/tapebackup/ISS/index.html
  http://www.hp.com/go/automation
  http://h18006.www1.hp.com/storage/saninfrastructure/hba.html
Availability, first customer ship, ready for volume shipment, changes in ordering process
Notes: <header>
<date/time>
Order, configuration, and licensing rules
    This section lists some of the steps required to configure a Factory Integrated Model. To ensure only valid configurations are ordered, HP recommends the use of an HP approved configurator. Contact your local sales representative for information on CTO product offerings and requirements. Configure-to-order servers must start with a CTO Chassis. This product offering does not support HP Factory Express Server Configuration Level 1. FIO indicates that this option is a Factory Installable Option.
    Step 1: Base Configuration
      HP ProLiant DL160 G5 Non- Hot Plug SATA Rack CTO Chassis
      HP ProLiant DL160 G5 Hot Plug SAS/SATA Rack CTO Chassis
    2: Choose Required Options
      Processors
      Memory
      Hard Drives
      Storage Controller
      Power supply
    Step 3: Choose Additional Options for Factory Integration
      ProLiant Essentials Offering
      Optical Drives
      Graphic Cards
      Communications
      Rack Kits
      Tape Drives
      HP D2D Backup System
      Tape Autoloaders
      Tape Libraries
      Service and Support Offerings (HP Care Pack Services)

## Slide 19: Attach recommendations
Base model
  Two models to choose from
    HP ProLiant DL160 G5 Non- Hot Plug SATA Rack
    HP ProLiant DL160 G5 Hot Plug SAS/SATA Rack
What options are associated with this product or solution?
  Performance
    Intel Xeon Quad-core 5400 sequence
      Up to 3.00GHz, 120W, 1600MHz FSB, 12MB
    HP Smart Array E500/256MB Controller (Standard RAID 0,1, 1+0)
      256MB Battery-backed write cache upgrade for RAID 5 support
    PCI Express communications
      1 Port Gigabit
      Dual Port Gigabit
      Quad Port Gigabit
      Multifunction Gigabit
      Dual Port Multifunction
      10 Gigabit Server
      HP IB 4X DDR PCI-e DUAL PORT HCA
      HP IB 4X DDR PCI-e SINGLE PORT HCA
      Myrinet PCI 2XP Rev-E 4MB
    PCI-X Riser Options
  Reliability and efficiency
    Optional 1200W high-efficiency power supply
  Management
    ProLiant Essentials Rapid Deployment Pack
    HP Server Migration Pack – Universal Edition
    ProLiant Essentials Virtual Machine Management Pack
    Lights-Out 100i Select Pack and Advanced Pack
  Storage
    Hard disk drive upgrades
      SATA non-hot plug hard drives up to 250GB
      SATA hot-plug hard drives up to 750GB
      SAS hot-plug hard drives up to 300GB
    Recommendations and best practices [for disaster recovery and backup]
      Tape Drives
      HP D2D Backup System
      Tape Autoloaders
      Tape Libraries
    Storage controllers
      HP 8 Internal Port SAS HBA with RAID
      HP Smart Array P400/256 Controller
      HP Smart Array P400/512 Controller
      HP Smart Array P800 Controller
      HP Smart Array P-Series 512MB BBWC Kit
    HP Care Pack Services
Notes: <header>
<date/time>
Attach recommendations

## Slide 20: Administration and management
Management and administration tools
  Lights-Out 100 management
    Several different licensing options are available
      LO100i Advanced Pack
      LO100i Select Pack
      LO100i Standard
    LO100i Advanced or Select Licenses are needed to activate advanced features
    Flat Pack or Electronic Key Delivery licenses are now available
Notes: Administration and management
    HP Lights-Out 100 Remote Management, it is a cost-effective, entry level remote management solution for the ProLiant 100 series servers. It is intended to provide standards based remote control that is consistent with the overall strategy for ProLiant 100 series servers - simple and affordable computing.
    Lights Out 100 is based on the IPMI standard.
      IPMI is the abbreviation for Intelligent Platform Management Interface and is an Intel-driven, server management effort that delivers hardware management to the cost-sensitive server market.
    Lights-Out 100 Remote Management
      Basic, affordable, continuous remote control that comes in several flavors to complement the ProLiant 100 series that you see reflected in this slide:
    Whereas the ML series is suited for SMB environments and single-tier architectures you will see typically a requirement for the Lights Out 100 Standard or the Lights Out 100c which is a mezzanine card for tower servers.
      LO100i Standard is basic remote management via unsecured interfaces
      LO100c Card is remote management via unsecured interfaces
    Whereas the DL series is suited for HPC and HPTC environments, you will see typically customers choose to acquire Lights Out 100i Advanced or Select Packs.
      LO100i Advanced is a cost-effective, secure remote control complete w/ embedded KVM over IP
      LO100i Select is a essential, secure remote control with remote serial console
    Regardless of whether you choose Lights Out 100c or Lights Out 100i, you get control of your Power, KVM/serial consoles, USB storage and the ability to monitor system Health and logs

## Slide 21: Product questions and answers
  Is it important that you have quad core processing capability, yet an affordable price?
    The DL160 G5 combines affordability, density, and manageability with the performance advantage of Intel Xeon quad-core processors.
  Need large amounts of local storage with dual processor capability, all in a dense form factor?
    The DL160 G5 supports four 3.5” drives for internal storage capacity of up to 3TB.
  Where can I find more information regarding the HP ProLiant DL160 G5?
    http://h10010.www1.hp.com/wwpc/pscmisc/vac/us/en/sm/proliant/proliant-dl.html
Notes: <header>
<date/time>
Product questions and answers