## Slide 1: Sun Configurations on FC-AL

## Slide 2
Sun Solaris Configuration FC-AL
500m
HSG80 FC Single Controller
Hub
Single Controller,
1 active port
500m
P1 Active
Sun
Solaris Server
For Solaris 2.5.1 and 2.6
16 LUNS (Default)
64 LUNS (Maximum)
Single Server / Single Controller
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3
Dual Redundant
Controller,
Transparent
Failover Mode
Sun
Solaris Server
HSG80 FC Dual Controller
Hub
500m
500m
Sun Solaris Configuration FC-AL
Single Server / Dual Controller
P1 Active
500m
P1 Standby
For Solaris 2.5.1 and 2.6
16 LUNS (Default)
64 LUNS (Maximum)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4
Single Controller,
2 active ports
No Failover
HSG80 FC Single Controller
Hub
P1 Active
P2 Active
500m
500m
Sun Solaris Configuration FC-AL
Single Server / Single Controller Dual-Port (Active,Active)
Sun
Solaris Server
For Solaris 2.5.1 and 2.6
32 LUNS (Default)
128 LUNS (Maximum)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
Dual Redundant
Controller,
Transparent
Failover Mode
HSG80 FC Dual Controller
Hub
P1 A
A
S P2
S
500m
500m
Sun Solaris Configuration FC-AL
Single Server / Dual Controller Dual-Port (Active,Standby)
Sun
Solaris Server
For Solaris 2.5.1 and 2.6
32 LUNS (Default)
128 LUNS (Maximum)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6
2 Dual Redundant Controller Pairs
Transparent Failover Mode
Hub
HSG80 FC Dual Controller
HSG80 FC Dual Controller
P1 A
A
P1A
A
S
S P2
S
S P2
500m
500m
Sun Solaris Configuration FC-AL
Single Server / (2) Dual Controllers /Dual-Port (Active,Standby)
Sun
Solaris Server
For Solaris 2.5.1 and 2.6
64 LUNS (Default)
256 LUNS (Maximum)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7
Sun
Solaris Server
Sun
Solaris Server
HSG80 FC Single Controller
Hub
Hub
Single Controller,
2 active ports
No Failover
500m
500m
500m
500m
P1 Active
P2 Active
Sun Solaris Configuration FC-AL
Dual Servers / Single Controller
For Solaris 2.5.1 and 2.6
32 LUNS (Default)
128 LUNS (Maximum)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8
Sun
Solaris Server
Sun
Solaris Server
HSG80 FC Dual Controller
Hub
Hub
500m
500m
500m
P1 Active
P1 Standby
P2 Standby
P2 Active
Sun Solaris Configuration FC-AL
Dual Servers / Dual Controllers
For Solaris 2.5.1 and 2.6
32 LUNS (Default)
128 LUNS (Maximum)
Dual Redundant
Controller,
Transparent
Failover Mode
Notes: <number>
<footer>
<header>
<date/time>