Software Manual DigiBoard PC/Xe and MC/Xe 
Intelligent Asynchronous Serial Communications Boards 

OS/2 Introduction 

The DigiWARE device driver for the OS/2 operating system supports the entire 
line of DigiBoard intelligent serial communications boards. The OS/2 device
driver takes all of its configuration information from the DEVICE= command
line in CONFIG.SYS, and all DigiBoard intelligent products in a system are
configured from a single command line. In addition to the device driver, the
configuration utility, DMODE.EXE is provided to change communication parameters
for individual ports without rebooting. DMODE.EXE is similar to the OS/2 MODE
command, but has some added features, and supports communications devices
beyond OS/2's range of COM1 to COM8. 
 
The OS/2 device driver for DigiBoard intelligent boards 
supports OS/2 applications only.  The device driver cannot 
be accessed from a virtual DOS window.
 
OS/2 provides two native Com device drivers for communication with non 
intelligent serial ports (e.g. COM1 and COM2).  These drivers are COM.SYS, the 
OS/2 native Com port driver, and VCOM.SYS, the virtual DOS window Com port 
driver.  These drivers cannot control intelligent serial devices. 

Software Installation 
The OS2 directory of the device driver diskette contains all of the files and 
documentation needed to install the OS/2 driver in your system. A list of 
these files follows: 

XALL.SYS      The installable device driver. 
DMODE.EXE     A MODE work-alike program for configuring serial ports
DMODE.DOC     Instructions for the DMODE program. 
DMODE.C       Source code for the DMODE program. 
INSTALL.DOC   Complete OS/2 installation doc (this file is a subset of it)
RELNOTES.DOC  Release notes. 
XALL.DOC      Programmer's infor about the driver and applicable system calls. 
*.BIN	      Miscellaneous binary files used by the driver. 

Copy all of the files from the \OS2 directory of the distribution diskette to
a single directory on your hard drive.  By default, driver and data files are
expected to be in \DIGI.   

Loading the Device Driver 

The device driver is invoked by placing its name and configuration arguments
into the system's CONFIG.SYS file.  All DigiBoard intelligent serial boards
must be installed from a single command line, which contains complete set-up
information for each board.  The general format of the command line is shown
in the box at right. The only required parameters are the board's I/O port
address and memory start address (see Examples 1 and 2).   
 
Command Line Examples 
General Format: 
DEVICE=\DIGI\XALL.SYS [/N:names] [/F:digipath] [/B:baud] [/D:data_type] [/A:A] 
[/V:message_file] /P:port /M:mem [, /P:port /M:mem] [, ...] 
 
Example 1: Single PC/Xe or MC/Xe board, basic installation 
DEVICE=\DIGI\XALL.SYS /P:320 /M:D0000 
 
Example 2: Two boards, basic installation 
DEVICE=\DIGI\XALL.SYS /P:320 /M:D0000, /P:300 /M:D0000 
 
Example 4: Single board, ports named digi1, digi2, etc.  
DEVICE=\DIGI\XALL.SYS /N:"DIGI"1 /P:320 /M:D0000 
 
Example 5: Single board, ports named com5, com6, etc.  
DEVICE=\DIGI\XALL.SYS /N:5 /P:320 /M:D0000 
 
The command line must appear on a single line in the CONFIG.SYS file.
This line may be up to 255 characters long.

Global Parameters 
The first six parameters in the command line are global parameters, and affect
all boards installed.  These parameters are optional, and may be omitted. If
omitted, default values will be used. 

/N:names 
Defines the naming convention to be use for the DigiBoard ports.  names 
consists of an optional "stem" followed by the starting device number.  The 
new stem must be enclosed in double-quotes ("").  If the stem is omitted, 
"COM" will be used.  If the number is omitted, "3" will be assumed.  If the /N 
parameter is not specified, the default name COM3 will be assigned to the first 
port. 
  /N:"DIGI"0 
  DIGI0, DIGI1, ... DIGIn 
  /N:4 
  COM4, COM5, ... COMn 
  /N:"QDEV" 
  QDEV3, QDEV4, ... QDEVn 

/F:digipath 
Defines an alternative directory for the location of the binary files (*.BIN),
if different from the location of the driver file, XALL.SYS. 

/B:baud 
Sets the default baud rate to be used for all ports.  If this parameter is not 
specified, all ports will be set to the OS/2 default of 1200 baud.  Since most 
OS/2 applications initialize the ports each time they are run, this parameter
is usually not necessary. 
  /B:9600 
  Initializes all ports to 9600 baud. 

/D:data_type 
Initializes all ports to the specified data type (parity, character length and 
number of stop bits).  If this parameter is omitted, the OS/2 default data type
of even parity, 7 data bits and 1 stop bit will be used.  The syntax is pds,
where p is E (even parity), O (odd parity) or N (no parity), d is 8, 7, 6 or
5, and s is 1 or 2. All three values must be specified, in the correct order.
Since most OS/2 applications initialize the ports each time they are run, this
parameter is usually not necessary. 
  /D:N81 
  Initializes all ports to no parity, 8 data bits and 1 stop bit. 
 
/A:A 
Initializes all ports to use alternating wiring for the DCD (Data Carrier
Detect) signal.  This swaps the functions of DCD (Data Carrier Detect) and
DSR (Data Set Ready) to make DCD available on an 8-pin RJ-45 connector. This
parameter is necessary only when connecting modems to RJ-45 equipped DigiBoard
products.  See the Connecting Peripherals section of the Installation Guide
for your board for more details. 

/V:message_path 
Forces banner and all verbose messages to be written to the specified file 
instead of the screen.  If /V: is given without a filename, messages will be 
written to \XALL.MSG.  Without this flag, all messages will appear on the 
system console.  The message file is overwritten each time the system is 
started. 
  /V:\ERRMSG 
  Banner and all messages are written to the file \ERRMSG. 
  /V: 
  Banner and all messages are written to the file /XALL.MSG. 

Per-Card Parameters 
The remaining two parameters are per-card parameters, and are used to inform
the driver of the type of board and where it is to be addressed in the host's
I/O and memory buses. These parameters are mandatory, and must be given for
each board! The per-card parameters must be given in complete sets, and the
sets must be separated by commas. 

/P:port 
Defines the I/O port address for the card. 
/P:300 
Board is addressed at I/O port 300h. 

/M:mem 
Dual-ported memory starting address.  This is the full 32-bit hexadecimal 
address of the beginning of the board's dual-ported memory. 
/M:D0000	 
Sets dual-ported memory start address to 0D0000h (in the BIOS 
expansion area between 640K and 1 megabyte). 
/M:E80000 
Sets start address of E80000h (in the fifteenth megabyte). 
PC/Xe and PC/Xi boards may all share the same memory starting address.  
MC/Xi, MC/Xe and COM/Xi boards must each have unique memory ad-
dresses. 

Testing the Ports 
The simplest (and probably the best) way to check the driver and I/O conn-
ections is to connect an ASCII terminal to one of the ports and redirect some
output to that port. If the terminal is connected to COM3, try something like
the following: 

DMODE COM3 
This will verify that the driver can find the port_the port's parameters will
be displayed. 

DMODE COM3 OCTS=OFF ODSR=OFF 
This insures that the hardware handshaking signals CTS and DSR will not prevent
output_ we are not concerned with flow control at this time. 

DIR > COM3 
This redirects the current directory to COM3. 
The console should simply respond by repeating the C:\> prompt, and the current 
directory (in this case, C:\) will appear on the terminal. 
 
User Diagnostics 
The OS2 directory of the DigiWARE distribution diskette contains a serial port
test utility, DGOS2UD.EXE, which can be used to test any OS/2 serial device 
supported by a Physical Device Driver.  Documentation for DGOS2UD.EXE can 
be found in the file DGUDREAD.ME, in the same directory. 

Troubleshooting 
 
Be sure to run the Memory Map utility to find the required amount of available
address space, and the User Diagnostics (UD-CISC.EXE) to verify that the board
is working correctly.  See the Installation Tips section of the Installation
Guide for your board for details.

If the C:\> prompt doesn't reappear, and the system seems to be "hung", you 
probably used a memory start address that is being used by some other device,
or the board is not set for the address specified in CONFIG.SYS. Try a diff-
erent address. If it still hangs, try a different I/O port. If your computer
has a memory cache and the board's memory start address is above 1 megabyte,
try either dis- abling the cache or moving the board to a low-memory address
(D0000 is usually a good choice). 

It is also possible that a conflict exists with another device driver which
has been loaded via CONFIG.SYS. The XALL.SYS line should be placed near the
end of CONFIG.SYS, and must not be placed before the DEVICE=TESTCFG.SYS line. 

Due to potential device naming conflicts, the pair of lines 
DEVICE=\OS2\COM.SYS 
	and 
DEVICE=\OS2\VCOM.SYS 
may cause problems. Be sure that the XALL.SYS line is placed before these lines 
in CONFIG.SYS.  If the XALL.SYS driver generates an error message, try 
temporarily putting "REM" in front of the above two lines. If this works, there
is probably a naming conflict.  You may need to add a /N:name command line flag 
to the XALL.SYS line to force the driver to use a different base name or start
numbering the COM devices at 5 or above. 

If the C:\> prompt does reappear, but there is no output on the terminal
screen, there is probably a cabling problem.  Make sure that all cable plugs
are securely seated in their receptacles, and that they are configured
correctly (see the Connecting Peripherals section in the Installation Guide
for your board). If the terminal displays output, but the data on the screen
is garbled, the terminal is probably not set with the same baud rate and data
type as specified in CONFIG.SYS (or the defaults, if not specified). Verify
these settings. If everything checks out and you still have problems, there
could be a problem with your board.  Contact your distributor or DigiBoard
Technical Support for further assistance. 

Error Messages 
If, when the driver is loaded, it cannot find the board(s), or if they fail to
respond properly to commands, certain error messages may be sent to the console
.These error messages are defined below: 

Could not find BIOS file 
Could not find FEP file 
Could not find data file 
One or more files were missing from the digipath directory.  The default 
digipath directory is the directory containing XALL.SYS.  If you have loaded 
the driver and data files into different directories, that directory containing
the data files (*.BIN) must be specified in the XALL command line with the 
/F:digipath parameter. 

IO Port Not Responding 
I/O port address set incorrectly, or conflicting with some other device. Verify 
setting, or try a different address. 

DigiBoard BIOS Will Not Boot 
DigiBoard BIOS Will Not Respond 
DigiBoard FEPOS Will Not Boot 
BIOS on board will not respond to commands from the driver.  Typically due 
to a memory conflict, or a memory cache conflict.   

Driver Failed to Hook Timer 
System Cannot Allocate Memory 
A system call to OS/2 has failed. 

Invalid Command Line Arguments 
Syntax error in the command line in CONFIG.SYS.  Double-check your entries. 

Programming Information 
The \OS2\PROGINFO directory on the device driver diskette contains programming
examples and information on how to obtain OS/2 programming manuals from IBM.